## Slide 1: Midwest Regional Rocket Launch Competition High Power Rocket Prep and Launch

## Slide 2: Altimeter Usage & Electronic Deployment
Av bay and sled design and construction
Securing sled within the av bay
Securing components on the sled

## Slide 3: Altimeter Usage & Electronic Deployment
Vent hole sizing – there are different opinions on what the proper size and placement for altimeter vent holes, or static ports, are.
Vern Knowles' Altimeter Port Sizing Page
(http://www.vernk.com/AltimeterPortSizing.htm)
One rule of thumb for the static pressure port is to use a 1/4" diameter hole for every 100 cubic inches in the altimeter bay compartment that is being vented. In general it is better to have multiple smaller holes, rather than one big hole.

## Slide 4: Testing
Ground testing of electronics and ejection charges
Show video of ground test
Be sure to follow safety procedures when testing ejection charges. Make sure that the area in front and behind the rocket is clear before arming the system. Also be aware that e-matches may use such low current that they can be fired by merely arming some model rocket launch controllers.

## Slide 5: Testing
Ejection charge sizing – there are many different ideas on the correct amount of powder for ejection charges. Make an initial estimate and then test it. Modify the amount based on the test and repeat until it works successfully.
Rocketry Online Ejection Charge Sizing Page
(http://www.info-central.org/?article=303, also includes info on shear pins)
Vern Knowles' Ejection Charge Sizing Page
(http://www.vernk.com/EjectionChargeSizing.htm)

## Slide 6: Testing
Using the ideal gas law PV = NRT and assuming a force of 15 psi you get
N = 0.006*D2L (grams)
where D is the diameter in inches and L is the length in inches of the compartment in the rocket that is to be pressurized. N is the size of the ejection charge in grams. For large diameter rockets you may want to use a lower psi, so the formula would be different.

## Slide 7: Testing
Test flights, with and without electronic deployment
Using data from flights on smaller motors to improve simulation of the final contest flight

## Slide 8: Basics of Rocket Prep and Flight
Show video of Chris flying his rocket?
Vent parachute compartments to avoid pressure separation
Make sure of snug fit of couplers and nosecones to avoid drag separation, or use shear pins
Igniters

## Slide 9: Basics of Rocket Prep and Flight
Pad safety
  The deployment system should not be turned on until the rocket is loaded on the pad.
  Turn on the deployment system, altimeter, etc., from outside the rocket. The rocket should be completely ready to fly before the electronics are powered on.
  Turn on the deployment system, and check that it is working, before inserting the igniter.

## Slide 10: Basics of Rocket Prep and Flight
Recovery system protection – (wadding, parachute and shock cord protectors)
Motor retention
Check list(s) – Make a check list with all of the steps listed. Have one team member check off the items on the list while the other team members perform the operations.